## Slide 1: CE801- Intelligent Systems and Robotics
Muhammed Baris Govercin
2501385

## Slide 2: PID Controller (Right Edge Following)
Sensors Used
Right LiDAR => [21:80]
Front LiDAR => [110:130] for safety stop
Why These Sensors?
Right sector gives stable wall-distance measurement
Front sector prevents collision during PID control
Tuning Process (kp, ki, kd)
Start with kp only → increase until fast but slightly oscillatory
Added kd → reduces wobble, smooths reaction
Added very small ki → removes constant bias if robot drifts
Final values:
  kp = 0.88, kd = 0.33, ki = 0.000

## Slide 3: Right Edge Following FLC: Sensors
Sensors Used
Right LiDAR => main wall-following input
Front LiDAR => detects blocked path to slow and turn
Left LiDAR => contextual awareness
Why These Sensors?
Right distance defines "desired wall distance"
Front prevents collision during fuzzy steering
Same LiDAR segmentation used across all controllers
(Based on Fuzzy_Right_Edge_Following.py)

## Slide 4: Right Edge Following FLC: Input Membership Functions
Right Distance Membership Functions
Close: (0 => 0.6)
Okay: (0.3 => 0.9)
Far: (0.7 => 1.2+)
Front Distance MFs
Near: (≤0.3 high, fades when 0.6)
Far: (starts increasing at 0.5)

## Slide 5: Right Edge Following FLC: Rule Base
Rule | IF | THEN (Angular) | THEN (Linear)
1 | Front Near | Strong Left | Very Slow
2 | Front Far & Right Close | Soft Left | Medium
3 | Front Near & Right Far | Soft Right (For REF) | Medium
4 | Front Far & Right Okay | Straight | Fast
5 | Front Far & Right Far | Strong Right | Medium-Fast

## Slide 6: Right Edge Following FLC: Output MFs
Angular Velocity Centroids
+0.8 Strong Left
+0.5 Soft Left
−0.5 Soft Right
0 Straight
−0.8 Strong Right
Linear Velocity Centroids
0.08 => Very Slow
0.18 => Medium
0.30 => Fast
0.25 => Medium-Fast

## Slide 7: Obstacle Avoidance FLC: Sensors
Sensors Used
Front LiDAR (101–132)
Right LiDAR (0–81)
Left LiDAR (132–242)
Why These Sensors?
Large front sector captures most collisions
Right/left sectors detect corridors, corners
Combined view enables smooth escape behaviour also prevent front left corner crash
(Based on Fuzzy_Obstacle_Avoidance.py)

## Slide 8: Obstacle Avoidance FLC: Membership Functions
Front Distance
Near: obstacle close
Far: front is clear
Side Distances
Close: wall/obstacle near
Open: free to turn
Goal
Avoid collision by choosing safest turning direction

## Slide 9: Obstacle Avoidance FLC: Rule Base
Rule | Condition | Behaviour
Corner Escape | Front Near & Both Sides Close | Strong Left + Stop
Turn Left | Front Near & Left Open | Normal Left
Soft Left | Front Near & Right Open | Soft Left (no right turns allowed)
Forward | Front Far | Move Straight

## Slide 10: Obstacle Avoidance FLC: Output MFs
Angular Centroids
1.0 Strong Left
0.6 Normal Left
0.3 Soft Left
0.0 Straight
Linear Centroids
0.0 Very Slow (corner escape decreases the probability of crash)
0.10 Slow turn
0.30 Straight motion

## Slide 11: Control Architecture (Blended FLC + PID)
Inputs for Control Architecture:
Right Distance
Left Distance
Front Distance
Justification:
Provides symmetrical understanding of corridor environment
Allows blending between Right Edge Follow and Obstacle Avoidance
Architecture Operation:
If front obstacle is very near => Obstacle Avoidance dominates 100%
If front is clear => Weighted blending:
  Weight(OA) = high when obstacle slightly near
  Weight(REF) = high when path is clear
Angular/linear velocities computed via weighted average
(Based on Final_Architecture.py)